Solutions of ”counting problem”
Chi-Kit Pao

# Solution via matrix multiplication
The problem from YouTube video "Olympiad level counting - How many subsets of {1,…,2000} have a sum divisible by 5" by 3Blue1Brown (url: https://www.youtube.com/watch?v=bOXCLR3Wric) can be described via matrix multiplication.
We want to name the counts of sums congruent to (0, 1, …, d-1) modulo d (d=5 in the video) as c_0, c_1, dotsaxis c_{d-1}.
As per definition in video, an empty set has a sum of 0 and is a multiple of d.
If we know the counts c_0, c_1, dotsaxis c_{d-1}. in a set of given numbers (set C), and we’ve got another set with counts a_0, a_1, dotsaxis a_{d-1}. (set A), the total counts t_0, t_1, dotsaxis t_{d-1}. for the union (set T) of these two sets will be (e. g. d=5):
left ( matrix{t_0 ## t_1 ## t_2 ## t_3 ## t_4} right) = left ( matrix{c_0 # c_4 # c_3 # c_2 # c_1 ## c_1 # c_0 # c_4 # c_3 # c_2 ## c_2 # c_1 # c_0 # c_4 # c_3 ## c_3 # c_2 # c_1 # c_0 # c_4 ## c_4 # c_3 # c_2 # c_1 # c_0} right ) cdot left ( matrix{a_0 ## a_1 ## a_2 ## a_3 ## a_4} right) .
For example, for the count of sums congruent to 2 in the new set T, we can combine:
- sums congruent to 2 from set C and sums congruent to 0 from set A,
- sums congruent to 1 from set C and sums congruent to 1 from set A,
- sums congruent to 0 from set C and sums congruent to 2 from set A,
- sums congruent to 4 from set C and sums congruent to 3 from set A, and
- sums congruent to 3 from set C and sums congruent to 4 from set A.
In total, it will be c_2 cdot a_0 + c_1 cdot a_1 + c_0 cdot a_2 + c_4 cdot a_3 + c_3 cdot a_4 , which is third row (t2) from the result of matrix multiplication.
## Calculation for any number
First of all, we know that for an empty set, there is one sum (= 0), so c0 is 1 and c1 = c2 = c3 = c4 = 0.
Then we combine this set with a set with only the number “1”. We’ve got two possibilities here to:
- either don’t use the new number (congruent 0 mod 5, a0=1), or
- or use the new number (congruent 1 mod 5, a1=1).
So for the new set as union of empty set and number “1”, we’ve got the following new counts in a solution vector.
left ( matrix{t_0 ## t_1 ## t_2 ## t_3 ## t_4} right) = left ( matrix{1 # 0 # 0 # 0 # 0 ## 0 # 1 # 0 # 0 # 0 ## 0 # 0 # 1 # 0 # 0 ## 0 # 0 # 0 # 1 # 0 ## 0 # 0 # 0 # 0 # 1} right ) cdot left ( matrix{1 ## 1 ## 0 ## 0 ## 0} right) = left ( matrix{1 ## 1 ## 0 ## 0 ## 0} right) .
It works similarly when combining this set with number “2”:
left ( matrix{t_0 ## t_1 ## t_2 ## t_3 ## t_4} right) = left ( matrix{1 # 0 # 0 # 0 # 1 ## 1 # 1 # 0 # 0 # 0 ## 0 # 1 # 1 # 0 # 0 ## 0 # 0 # 1 # 1 # 0 ## 0 # 0 # 0 # 1 # 1} right ) cdot left ( matrix{1 ## 0 ## 1 ## 0 ## 0} right) = left ( matrix{1 ## 1 ## 1 ## 1 ## 0} right) .
For sets with 3, 4, and 5 numbers:
n=3: left ( matrix{t_0 ## t_1 ## t_2 ## t_3 ## t_4} right) = left ( matrix{2 ## 2 ## 1 ## 2 ## 1} right),n=4: left ( matrix{t_0 ## t_1 ## t_2 ## t_3 ## t_4} right) = left ( matrix{4 ## 3 ## 3 ## 3 ## 3} right), n=5: left ( matrix{t_0 ## t_1 ## t_2 ## t_3 ## t_4} right) = left ( matrix{8 ## 6 ## 6 ## 6 ## 6} right) .
For sets with numbers n > 5, we can repeat the matrix generation and matrix multiplication with the solution vector for n=5. If there is remainder for n divided by 5, we will apply another matrix multiplication with solution vector of n=1, …, 4.

For n = 2000, we will need 2000 / 5 = 400 steps.

But we can also calculate solution vectors for n=51, 52, 54, etc. by multiplying the generated matrix with the new solution vector coming out from the matrix multiplication.
For n = 2000 = 5 * 400 and 400 = 1 1001 0000b, we need to multiply with solution vectors of 516, 5128, and 5256.

# Solution via generating function
In the YouTube video "Olympiad level counting - How many subsets of {1,…,2000} have a sum divisible by 5" by 3Blue1Brown (url: https://www.youtube.com/watch?v=bOXCLR3Wric), it shows a solution by using a generating function:
f(x) = ( 1+x )( 1+x^2 )( 1+x^3 )...( 1+x^2000 ) newline f( x ) = sum from{n=0} to{N} c_n x^n = 1+x+x^2+2x^3+2x^4+... .
With %zeta = e^{{2%pi i} over {5}} , the sum f(ζ0)+f(ζ1)+f(ζ2)+f(ζ3)+f(ζ4) results in 5 times of the sum of coefficients which is multiple of 5:
f( %zeta^0 ) + f( %zeta^1 ) + f( %zeta^2 ) + f( %zeta^3 ) + f( %zeta^4 ) = 5 cdot left( c_0 + c_5 + c_10 + ... right )
For numbers n which is multiple of 5, the video gives the answer that there are 1 over 5 left( 2^n + 4 cdot 2^{n over 5} right ) sums which are divisible by 5. E. g. for n=2000, there are 1 over 5 left( 2^2000 + 4 cdot 2^400 right ) of them.
This approach works similarly with every divisor d >= 2 and when n is multiple of d.
## Calculation for remainder of sums other than 0
I’ve have modified this approach by adding factors while adding the generating functions. With %alpha_{l,k} = %zeta^{k(d-l)} and k is the remainder of sums when dividing by d (e. g. 5), the sum α0,kf(ζ0)+α1,kf(ζ1)+α2,kf(ζ2)+α3,kf(ζ3)+α4,kf(ζ4) results in 5 times of the sum of coefficients with remainders is k = (0, …, 4) when divided by 5:
k=0: %alpha_{0,0} f( %zeta^0 ) + %alpha_{1,0} f( %zeta^1 ) + %alpha_{2,0} f( %zeta^2 ) + %alpha_{3,0} f( %zeta^3 ) + %alpha_{4,0} f( %zeta^4 ) = 5 cdot left( c_0 + c_5 + c_10 + ... right ) newline k=1: %alpha_{0,1} f( %zeta^0 ) + %alpha_{1,1} f( %zeta^1 ) + %alpha_{2,1} f( %zeta^2 ) + %alpha_{3,1} f( %zeta^3 ) + %alpha_{4,1} f( %zeta^4 ) = 5 cdot left( c_1 + c_6 + c_11 + ... right ) newline k=2: %alpha_{0,2} f( %zeta^0 ) + %alpha_{1,2} f( %zeta^1 ) + %alpha_{2,2} f( %zeta^2 ) + %alpha_{3,2} f( %zeta^3 ) + %alpha_{4,2} f( %zeta^4 ) = 5 cdot left( c_2 + c_7 + c_12 + ... right ) newline k=3: %alpha_{0,3} f( %zeta^0 ) + %alpha_{1,3} f( %zeta^1 ) + %alpha_{2,3} f( %zeta^2 ) + %alpha_{3,3} f( %zeta^3 ) + %alpha_{4,3} f( %zeta^4 ) = 5 cdot left( c_3 + c_8 + c_13 + ... right ) newline k=4: %alpha_{0,4} f( %zeta^0 ) + %alpha_{1,4} f( %zeta^1 ) + %alpha_{2,4} f( %zeta^2 ) + %alpha_{3,4} f( %zeta^3 ) + %alpha_{4,4} f( %zeta^4 ) = 5 cdot left( c_4 + c_9 + c_14 + ... right )
For k=0, the formula 1 over 5 left( 2^n + 4 cdot 2^{n over 5} right ) remains the same since all factors %alpha_{l,0} equal to 1. For k=1..4, we’ve got the formula 1 over 5 left( 2^n - 2^{n over 5} right ) for number of sums with remainder k when divided by 5.
This approach works similarly with every divisor d >= 2 and when n is multiple of d. If n is not a multiple of d, we’ll have to apply matrix multiplication with solution vector of n=1, …, d-1 (see 1.1).